## Slide 1: perfSONAR toolkit basics
This document is a result of work by the perfSONAR Project (http://www.perfsonar.net) and is licensed under CC BY-SA 4.0 (https://creativecommons.org/licenses/by-sa/4.0/).
eduPERT workshop — TNC18
Antoine Delvaux, PSNC
14-06-2018

## Slide 2: Outline
Workshop lab setup
perfSONAR toolkit web interface
Running measurements/tests

## Slide 3: Workshop lab setup
VM
  Don’t do that for real deployments!
SWITCHengines
  OpenStack, firewall, IPV4 NAT
10 VM x 3
  perfSONAR toolkit 4.0.2
  perfSONAR toolkit 4.1-beta (pre-beta)
  Nagios XI

## Slide 4: Accessing the VM
Group in pairs
Web admin access
  Username: psadmin
  Pass: edupert
ssh access
  Username: edupert
  Pass: to be distributed during the workshop

## Slide 5: Outline
Workshop lab setup
perfSONAR toolkit web interface
Running measurements/tests

## Slide 6: Configuring pS toolkit
See sheets with VM details
We will go through the toolkit configuration pages
And set up some measurements
Notes:   First ask if they’re familiar with the toolkit UI
    If yes, then skip
    If not, then go through some examples

## Slide 7: Configuration - Web
We can do most other things via the web interface once we have a user that can auth against it
  do-it-yourselfers can still hand edit config – we just won’t deal with that here
Some things we care about:
  Administrative info (See our privacy policy)
  NTP (time keeping)
  Configuring some tests (directly)

## Slide 8: Configuration - Web

## Slide 9: Authentication
The user you created will need to authenticate to make system level changes.
The machine has a self-signed (e.g. ‘lame’) certificate, so be aware of that:
9 – 6/12/18, © 2013 ESnet, Internet2
J. Zurawski – zurawski@es.net

## Slide 10: Administrative Info
For the most part this is point and click – the system needs this so that it can be located, and so that certain services will start.
Notes: Everyone should do this, and be sure to enter lat/long info
Note that after this occurs – LS registration happens ‘automatically’ as long as the host is not in private space

## Slide 11: Lookup Service Integration
Once you complete the administrative info – your host will attempt to register with the “Lookup Service”
This is a global directory that makes it easier to find perfSONAR nodes.
If your host as the admin info present, and isn’t a private IP, it will do this automatically
Notes: Everyone should do this, and be sure to enter lat/long info
Note that after this occurs – LS registration happens ‘automatically’ as long as the host is not in private space

## Slide 12: NTP
Note that it may take a day to fully stabilize the clock
Pick 4 – 5 Close servers for NTP
We have a fast way to do this, or you can manually select
Can also add your own servers if you don’t like ours
Notes: Also a requirement. If your site is blocking NTP, use internal servers

## Slide 13: NTP
pScheduler and OWAMP require a very stable time source.
The toolkit interface allows you to configure your own host, or choose public ones we know of.

## Slide 14: Add some measurements
Measurements also called tests
We will go together through some examples

## Slide 15: CLI tools
Measurements tools are CLI based
  ping, traceroute, tracepath
  iperf
  owamp
Measurements scheduler (perfSONAR)
  pscheduler
Linux
  Text configuration files

## Slide 16: perfSONAR toolkit basics
This document is a result of work by the perfSONAR Project (http://www.perfsonar.net) and is licensed under CC BY-SA 4.0 (https://creativecommons.org/licenses/by-sa/4.0/).
eduPERT workshop — TNC18
Antoine Delvaux, PSNC
14-06-2018