## Slide 2: Outlines
Introduction to time and frequency distribution
  Definitions of time
  Why do we need it?
Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
  Redefinition of the second (SI)
  Existing alternatives to optical link?
Survey of the techniques (accuracy, TRL, etc.) and requirements to disseminate ultra-accurate time and ultra-stable frequency
Geneva at the crossroad of Europe
  Time and Frequency service(s) at multi-domain level in Europe (gateways)
  Advanced science cases and potential end-users at CERN

## Slide 3: Introduction to time and frequency distribution
  Definitions of time
  « Passive » definitions
    1889: redefined in terms of a day =>
    1956: redefined in terms of a year =>
  Based on matter
    1967: the duration of 9 192 631 770 periods of the radiation corresponding to the transition between the two hyperfine levels of the ground state of the cesium 133 atom
Coordinate time
  1972: TAI and UTC are obtained from a combination of 400 cesium clocks all around the world, sending their data to BIPM
  => Real legal time is calculated 15 days afterward
Gnomon 2300 BCE

## Slide 4: Introduction to time and frequency distribution
7 SI Base Unit with 7 constants to measure the world
Symbol | Name | Quantity | Definition
s | second | time | the caesium hyperfine frequency Cs
m | metre | length | the speed of light in vacuum c
kg | kilogram | mass | the Planck constant h NEW
A | ampere | electric current | the elementary charge e
K | kelvin | temperature | the Boltzmann constant k
mol | mole | amount of substance | the Avogadro constant NA
cd | candela | luminous intensity | the luminous efficacy of a defined visible radiation Kcd
Notes: The recommended practical system of units of measurement is the International System of Units (Système International d'Unités), with the international abbreviation SI.
What could be best achievable performances?

## Slide 5: Introduction to time and frequency distribution
Why is frequency measurement so important?
Quantity | Definition | Numerical value constants | Uncertainty
time | the caesium hyperfine frequency Cs | 9 192 631 770 Hz | 10−13
length | the speed of light in vacuum c | 299 792 458 m.s-1 | 4 × 10−9
mass | the Planck constant h | 6.626 070 15 × 10-34 m.s-1 | 1×10−8
electric current | the elementary charge e | 1.602 176 634 × 10−19 m.s-1 | 2.3 × 10−10
temperature | the Boltzmann constant k | 1.380 649 × 10−23 m.s-1 | 3.7 × 10−7
amount of substance | the Avogadro constant NA | 6.022 140 76 × 1023 lm.W−1 | 4.5 × 10−10
luminous intensity | the luminous efficacy of a defined visible radiation Kcd | 683 lm.W−1 | 10−4
Notes: The recommended practical system of units of measurement is the International System of Units (Système International d'Unités), with the international abbreviation SI.
Time (derivating from frequency measurements) has the best uncertainty

## Slide 6: Introduction to time and frequency distribution
Why do we need time?
Time (derivating from frequency measurements) has the best uncertainty
Dependancy to time of other SI
  => 5 out of the 6 other SI are built on the second
=> In all scientific domain, best measurements can only be done when based on frequency measurements
Societal impact
  GNSS (Global Navigation Satellite System)
  Telecommunications (6G)
  Smart grid
    Those 3 markets generate $700 billion/year
    If any project can increase by 1%: $7billion/year

## Slide 7: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
NMI A
Cesium and rubidium clocks (GNSS)
Distant sites
GPS link
GPS link
Me too! Let’s compare it to mine and have a look at their stability!
NMI B
Clock comparisons to establish a new standard
better than cesium
Hey fellow NMI, I got a new clock!
I was able to compare both signals to my own old reference => NMI « A » has better result
Notes: Because we want to produce better clocks

## Slide 8: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
NMI A
Cesium and rubidium clocks (GNSS)
Distant sites
GPS link
GPS link
…
Me too! Let’s compare them again
NMI B
Clock comparisons
  Plan A : Satellites
Brand new clock with much better results
It seems that your measurements have better quality than the transmission link… Can’t help you sorry…
Notes: Because we want to produce better clocks

## Slide 9: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe

## Slide 10: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
NMI A
Distant sites
NMI B
Clock comparisons
  Plan A: Satellites
  Plan B: Moving (complicated)
I come to you !

## Slide 11: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
NMI A
Distant sites = connected trough educational fibre network + crossborder fibre
NMI B
Clock comparisons
  Plan A: Satellites
  Plan B: Moving (complicated)
  Plan C: Technique through fibre… If only we could
Metrological projects | 
LIFT | REFIMEVE+
OPTIME | EMRP (EURAMET)
EMPIR | ICOF
OFTEN | CESNET E-Infrastructure…
GEO-Q | CLONETS
OTFN | …

## Slide 12: Main use-cases, comparing atomic clock for National Metrologist Institute in Europe
Clock comparisons
  Plan A: Satellites
  Plan B: Moving (complicated)
  Plan C: Technique through fibre, how so?

## Slide 13: Early conclusions
The second is one of the SI Units
  And is the one measured with best uncertainty
Second is used to define 5 other SI Units
Cesium clocks were best rulers in 1967 (13 digits) but we may have find better ones, several candidates (17 digits) but we need to compare NMI before adopting a new standard.
Better time means will help all science domains
New optical clocks have 4 orders of magnitude better results
The only existing way to compare them is based on optical fibre. There is no alternative.

## Slide 14: Situation in Europe
  1 country = 1 NMI => Europe has the best density of new atomic clocks in the world
    Numerous interconnections + small distances between NMI
    Require fibres…
  NRENs in Europe:
    They are incubators of revolutionary projects (IPv6, client/server and Cloud computing…)
    They constitute a distributed network across Europe
    Each NREN is connecting many Reasearch Infrastructure that want to benefit from such precise signals
You can now discuss and have an outstanding partnership for the greater good of Science!
NREN
You and NMI have liked each other!
NMI

## Slide 15: TRL of techniques
There has been several T/F projects during past 10 years to improve dissemination techniques
=> Up-time close to 80% in 2019, close to a service

## Slide 16: Example of T/F setup, optical link
ILA #2
ILA #1
Point Of Presence
Point Of Presence
Géant
Telecom equipment
Mux
T/F #2
T/F #1
Demux
Géant amplifier
T/F #2 Bidir amplifier
T/F #1 Bidir amplifier
T/F #2 RLS
T/F #1
Géant
Telecom equipment
Mux
T/F #2
T/F #1
Demux
T/F #1
T/F #2
Géant amplifier
T/F #2 Bidir amplifier
T/F #1 Bidir amplifier
T/F #1
T/F #2
OADM
T/F #2 Bidir amplifier
T/F #1 Bidir amplifier
OOB monitoring
OOB monitoring
OOB monitoring
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OADM
OOB monitoring
OOB monitoring
OOB monitoring
OOB monitoring
OOB monitoring
OOB monitoring
OOB monitoring
T/F #1 Bidir amplifier
T/F #2 Bidir amplifier
IB - OSC
T/F #1 Bidir amplifier
T/F #2 Bidir amplifier
IB - OSC
Géant Telecom equipment with line side
Routers with client-side signals (can en 10Gbps or 100Gbps…)
OSC client
OSC client
T/F signal 194,3THz (43rd channel ideally)
Optical transceiver for T/F signal in C-Band (ideally 43rd Channel)
Bidirectional L-band amplifier for T/F signal #1
T/F signal194,4THz (44th channel)
Fixed Optical Add-Drop Multiplexer (44th Channel)
Optical transceiver for T/F signal in 194,4THz
Bidirectional EDFA amplifier for T/F signal #2
OMS (optical Multiplexed Section)
Out Of Band monitoring
In Band monitoring through extraction of OSC (Optical Supervisory Channel)
OADM
Fixed Optical Add-Drop Multiplexer (C oband Channel)
T/F#3
T/F#3
T/F#3
Optical grey transceiver for T/F signal
SyncE 1588
SyncE 1588

## Slide 17: Example of T/F setup, zoom in ILA
Raman amplifier
Raman amplifier
Géant amplifier
OADM
T/F #2 Bidir amplifier
OADM
T/F #1 Bidir amplifier
T/F #2 Bidir amplifier
FC/APC
FC/APC
T/F #1 Bidir amplifier
FC/APC
FC/APC
FC/APC
?
?
?
FC/APC
?
FC/APC
FC/APC
OADM
OADM
FC/APC
?
?
?
FC/APC
?
10/100/1000Base-T
10/100/1000Base-T
10/100/1000Base-T
10/100/1000Base-T
OSC client port
FC/APC
FC/APC
FC/APC
FC/APC
FC/APC
FC/APC
?
?
?
?

## Slide 18: Some T/F Networks in Europe
Optime
ICOF
Deployed
About to be deployed
Future extensions
Notes: Friendly competition

## Slide 19: OTFN project to catalyze the emergence of metrological networks in Europe
  Objectives
  To study the challenges of creating a European T/F distribution service
  Focusing on holding several dissemination events
    More NRENs become aware of the potential of these new services for their users and communities.
Case of Geneva
At the crossroad of Europe
  RENATER, PSNC, GARR, SWITCH, NORDUnet, Géant
CERN
  Many potential end-users willing to have access to better precision

## Slide 20: T/F services a new challenge for NREN to improve all science domains
NMI
NMI
SI
Second
10−13
Current standard
SI second
10−17
Future
standard
NREN #1
NREN #2
Reasearch institutes
2
3
4
1 - Time is a central unit in science
2 – Better second improves all domain of science
3 – Comparisons through optical fibres required
4 – Some RI institutes who can benefit from these services are connected to NREN
Notes: Time is a central SI Unit
Improving its standard will impact measurement in all scientific domains
Necessity to run comparison campaigns in order to select the best optical clock to replace cesium clocks
Comparisons can only be made through optical fibre
NREN are key partner for those project
=> Europe is losing its leadership because scientists need fibres that we profide them too slowly

## Slide 22: OADMs thin films
?
FC/APC
?
FC/APC
Common port
Bidirectionnal T/F services
Express data port
200GHz
100GHz
?
FC/APC
?
FC/APC
Common port
Bidirectionnal T/F services
Express data port
200GHz
100GHz

## Slide 23: CLONETS project
to collect information (NMI, NREN, end-users);
to study applications beyond research infrastructures (societal applications);
to define roadmaps and strategies to support future European work;
  => economic potential of the future T/F market
create the environment necessary for future work (to define standards for international metrological network deployment);
to study the evolution of the partnership for a future exploitation phase of the created clock services network.
Acronym: CLONETS | Project ID: 731107
Topic: INFRAINNOV-2016 | Budget: 1 994 646 €
Start: 1st january 2017 | Duration: 30 months
Project manager: eva.bookjans@obspm.fr | Website: http://www.clonets.eu
Infos
Objectives:
Horizon 2020

## Slide 24: Icon set 1 (use them as much you can)
Users: Earth Observation
Users: Arts and Education
Users: Energy
Users: Health and Medicine
Users: Space
Users: Physics
User Groups
Cloud Services
Strategy and Vision
Schedule
TFs and SIGs
Storage
Real-Time Communications
GÉANT Logo
GÉANTPeople
GÉANT Services
Professional Services
GÉANT Network
GÉANT Community
Research Programmes
Connectivity and Network
Efficiency
EU Logo

## Slide 25: Icon set 2 (use them as much you can)
Latin America region
CAREN region
AC2 region
Asia Pacific region
EUMED region
North America
EaPConnect region
Glue
Vision
Strategy & Vision
Campus
Service cogs 1
Service cogs 2
Pilot
Production
Journal/Library
Developer
Legal
NREN
Finance
Events
Compass
Location