## Slide 1
  NFV PoC update
November, 2017
Wouter Huisman

## Slide 2: NFV?
Bron: F5 Networks Inc

## Slide 3: Virtualization variants
Appliances
  FPGA/Asic optimized for packet handling
  Proven track record, predictable performance
  SW and HW same supplier
Commodity Servers
  COTS
  Very flexible, any VNF possible
  Performance dependent on deployment
  New developments in HW
    NICs with DPDK support
    smartNIC Netronome
  Docker or VMs

## Slide 4: Deployment models
Centralized VM cluster
  More efficient and quickly ready for service
  Shared resources – more cost efficient
  Not suitable for all NFV functions
Distributed VM deployment
  Separate server at customer site or CPE with integrated x86
  Case by case deployment model

## Slide 5: vrouter in standard deployments
Source: http://fuel-plugin-contrail.readthedocs.io/en/latest/dpdk.html

## Slide 6: vrouter in DPDK deployments
Source: http://fuel-plugin-contrail.readthedocs.io/en/latest/dpdk.html

## Slide 7: Virtual network functions – Why?
Customers
  Need for more external service
  No tender needed
    Flexibility
    Scalable
    No vendor lock-in
    Easy to test NFV without commitment
SURFnet
  Providing added value to customers/ new services
  Providing added value / unburden our customers

## Slide 8: Virtual network functions – Why not?
Risks
  Little/no interest from customers
  Complex development cycle
  Performance issues VNF
    E2E services not realized easily
    Performance lower than anticipated
    Use VNF remains static
    Operationally difficult to manage

## Slide 9: Logical NFV setup

## Slide 10: Front…

## Slide 11: …back

## Slide 12: Problems
vMX behaved slightly different than MX
DPDK NICs
  Mellanox NIC niet supported by Contrail 3.2/4
  Intel x710 NIC bug
L2 networking clearly less well supported  L3

## Slide 13: Overview components – take 2
blade
Pica8 switch
blade
blade
blade
blade
blade
blade
Contrail
Server Manager
Adding hosts
Contrail
Controller
networking
SN7/8
MX104
Horizon GUI
Openstack
VM,NFV

## Slide 14: Contrail Server Manager
Load
  server-manager add server -f blade1.json
  Node name/IP adres/MAC adres/NIC IFs/DPDK/etc
Reimage
  server-manager reimage --server_id compute-node-01
Provision
  server-manager provision --server_id compute-node-01 contrail_4_0_0_3053
Result: a new node with a Linux load in cluster1 configured with vrouter ready in Horizon/Contrail
Contrail
Server Manager

## Slide 15: Contrail Controller
Create networks
Create security groups
Create policies
Connect Service Instance using Port Tuples
  VM spawning is split in two actions
Contrail
Controller

## Slide 16: Horizon
Horizon GUI
Openstack
VM spawnen
  Define name
  Template & settings
  Conect to network
  If needed, add Security Groups

## Slide 17: Demo physical layout
red-1
green-1
vSRX-1
right
left
green-2
Horizon GUI
Openstack
Contrail
Controller
Contrail
Server Manager
red-2

## Slide 18: Logical layout
Cirros
Green-1
Cirros
Red-1
192.168.20.12
vrouter
vrouter
Cirros
Green-2
vrouter
MPLSoUDP
192.168.20.13
192.168.10.12

## Slide 19: Ping between 2 networks
Cirros
Green-1
Cirros
Red-1
vrouter
vrouter
Cirros
Green-2
vrouter
MPLSoUDP
policy
192.168.20.12
192.168.20.13
192.168.10.12

## Slide 20: Ping via FW to remote network
Cirros
Green-1
Cirros
Red-1
vrouter
vrouter
Cirros
Green-2
vrouter
MPLSoUDP
vrouter
vSRX
policy
192.168.20.12
192.168.20.13
192.168.10.12

## Slide 21: Service stitching
Cirros
Green-1
Cirros
Red-1
vrouter
vrouter
Cirros
Green-2
vrouter
MPLSoUDP
vrouter
VNF2
vrouter
VNF1
policy
192.168.20.12
192.168.20.13
192.168.10.12

## Slide 22: Security Group
Cirros
Green-1
Cirros
Red-1
vrouter
vrouter
Cirros
Green-2
vrouter
MPLSoUDP
vrouter
vSRX
Security group: Only 30.30.30.0/24
policy
192.168.20.12
192.168.20.13
192.168.10.12

## Slide 23: To be investigated
Networking architecture
  Scalability, automated
Throughput
  Different FW vendor
Failover
Operating VNF by SURFnet
Configuration by customers
Orchestration